## Slide 1: Energy Efficiency Programs, Codes and Standards: What’s Happened in the SEE Action Era
Prepared for SEE Action by the
Electricity Markets and Policy Group
Lawrence Berkeley National Laboratory
July 2014

## Slide 2: Table of Contents
Utility Customer-Funded Efficiency Programs: Savings, Spending, Cost of Savings, and Behavioral/EM&V
ESCOs: Revenue Growth and Market Potential
Combined Heat and Power
Policies That Advance or Reduce Barriers to Energy Efficiency: Throughput Incentives and Savings Targets
Building Energy Codes and End-Use Standards
Energy-Use Disclosure Requirements
Efficiency Financing

## Slide 3: Estimated Achieved Annual Electricity Savings Rising Among States
30% of states achieving 1% or higher annual incremental electricity savings
Many “new” states – about 40% – are saving 0.2% to 0.7%
  Given the prevalence of rising targets, most of these states are poised for higher savings
Chart: Percent Electricity Savings in 2012
| 0.2% | 0.5% | 0.8% | 1.0% | 1.2% | 1.5% | 2.0% | More
 | 5 | 16 | 9 | 5 | 5 | 6 | 3 | 1
Source: Barbose et al. “The Future of Utility Customer-Funded Energy Efficiency Programs in the United States: Projected Spending and Savings to 2025” LBNL-5803E. 2013
Notes: This histogram shows the distribution among states of percent annual electricity savings levels that LBNL estimates were achieved in 2012 by all utility customer-funded programs, including those funded by publicly owned utilities and cooperatives, as well as investor-owned utilities. Nearly a third of states are saving at least 1% of electricity that would otherwise have been consumed. Below this level are a large number of states – about 40% - that mostly are relatively new to energy efficiency and are just ramping up their savings targets.

## Slide 4: 80% Growth in Total Electric & Gas DSM Spending (2008-2012)
2013 State of the Efficiency Program Industry:
Budgets, Expenditures, and Impacts, Consortium for Energy Efficiency, 2014
Notes: Spending on energy-efficiency programs funded by utility customers – for both gas and electricity – has increased 80% in the last five years, based up annual industry surveys of program administrators by the Consortium for Energy Efficiency. The rate of growth has slowed somewhat from the last decade, in part due to lower natural gas prices and therefore diminished program cost effectiveness, but LBNL projects spending will nearly double and could triple by 2025.

## Slide 5: Half of States Have Energy Savings Targets
EERS, Utility-Specific Target or All Cost-Effective Mandate
RPS/RES with Efficiency as an Eligible Resource
Source: ACEEE, Energy Efficiency Resource Standards: A New Progress Report on State Experience, April 2014. http://aceee.org/sites/default/files/publications/researchreports/u1403.pdf
Notes: Half of the states have some sort of policy that commits program administrators to acquiring a certain amount of savings each year, based on recent analysis by the American Council for an Energy Efficient Economy (ACEEE). These policies include energy efficiency resource standards (EERSs); savings targets that are tailored to each utility or program administrator; renewable portfolio or energy standards (RPS/RES) that allow energy efficiency as an eligible resource; or a statutory mandate for program administrators to acquire all cost-effective efficiency. The number of states with such policies was somewhat larger: Indiana eliminated its EERS; Florida funds its programs below what is necessary to meet its targets; Utah and Virginia have voluntary standards. And while Ohio technically has retained its policy, the state has frozen its savings targets at current levels and allowed a variety of other ways of meeting the targets, such as savings banked from earlier years and reduced line losses from new transmission and distribution investments.

## Slide 6: Most Leading States Projected to Save 1.5% or More
Source: Barbose et al. “The Future of Utility Customer-Funded Energy Efficiency Programs in the United States: Projected Spending and Savings to 2025” LBNL-5803E. 2013
Notes: The “Top 10” states, defined by savings, are all achieving more than 1%, and most are headed for 1.5% of more within the next year or two.

## Slide 7: Other States with Targets Generally Support Rising Savings Through 2020
Adapted and Updated from Barbose et al. “The Future of Utility Customer-Funded Energy Efficiency Programs in the United States: Projected Spending and Savings to 2025” LBNL-5803E. 2013
Notes: Most other states have savings targets or similar policy commitments that savings will rise at least through the end of this decade. Notable exceptions include the elimination or effective downward revision in savings targets for future efficiency program portfolios in Indiana and Ohio. The actual impact of those policy changes is not certain, but the changes do appear to eliminate or substantially undermine the regulatory impetus to acquire savings. We therefore have modeled future years based on declining annual incremental savings from customer-funded programs. Barring some reversal, both states appear headed for de minimis savings from programs near the end of the decade.

## Slide 8: Recent Changes in EERSs Are Likely to Impact the National Savings Trajectory
Notes: The policy changes in Indiana and Ohio – based upon our assumptions of declining annual incremental savings – do have a material impact on total national savings. We project that national electricity savings would decline from today’s levels.

## Slide 9: Most States Have Some Decoupling Mechanism in Place or Pending For At Least One Utility
Notes: This map, maintained by the Natural Resources Defense Council (NRDC), tracks decoupling policies for both electric and natural gas utilities. It indicates that about half of the states have or are contemplating decoupling revenues from sales for one or more gas or electric utilities, with decoupling for gas utilities being more prevalent.

## Slide 10: Expanding Behavioral Programs, Many Using SEE Action EM&V Protocols
Opower - largest implementer of normative behavioral programs
  More than 80 U.S. utilities and other efficiency program administrators
  12M households or one in 10 U.S. homes receive normative messaging
  ~1%-1.5% savings annually
  All projects employ SEE Action recommended protocols (randomized control trials)* for EM&V
*Todd, Annika, Elizabeth Stuart, Steven R. Schiller, and Charles A. Goldman. Evaluation, Measurement, and Verification (EM&V) of Residential Behavior-Based Energy Efficiency Programs: Issues and Recommendations. 2012.
Notes: In recent years, a number of program types or program components have emerged as important contributors to programmatic efficiency in terms of the numbers of program administrators offering those programs, the number of participants, program spending and in some cases the programs’ share of energy savings. These emergent programs or components include efficiency financing and a variety of behavioral programs. Normative behavioral programs have spread at a particularly rapid pace. These programs couple comparisons of customers’ energy use to that of similar consumers with suggestions for changes in consumption habits or installation of more efficient end uses. The largest implementation contractor, Opower, delivers these normative messages to one in every 10 U.S. households and is used by more than 80 utilities and other program administrators that together serve more than 90% of U.S. households.
The SEE Action EM&V Working Group in a 2012 report observed that behavioral programs pose certain measurement and verification challenges and recommended that behavioral programs use randomized controlled trials in order to arrive at robust and unbiased estimates of program savings. All Opower programs employ this methodology so that one of the most prevalent acquisition strategies for savings acquisition in the residential sector now generates savings estimates that are the “gold standard” for EM&V.

## Slide 11: Average Program Administrator Cost of Saved Energy for Commercial & Industrial Efficiency Programs Low for 2009-2011
The most common C&I programs (General Custom and Prescriptive) had a savings-weighted average cost to the program administrator of less than two cents per kWh for 2009-2011
Values in this figure are based on the 2009-2011 data in the LBNL DSM Program Impacts Database. CSE values are for program administrator costs and based on gross savings. Savings are levelized at a 6% real discount rate. The savings-weighted average CSE is calculated using all savings and expenditures at the level of analysis. The inter-quartile range and median CSE values are calculated for each program type.
Notes: Saving energy through utility customer-funded programs remains, on average, fairly inexpensive. Nationwide, the savings-weighted average cost across all program types was about 2.1 cents per kilowatt-hour in the 2009-2011 period, based upon data collected by LBNL from more than 30 states. The lowest cost programs are in the commercial and industrial sector, where the savings-weighted average for the most prevalent custom and prescriptive program types was less than two cents per kilowatt-hour. For the more prevalent C&I program types, the chart indicates the interquartile range (the middle 50%) of costs and the number of programs in the sample. The chart indicates that the median costs for these most common C&I programs also are relatively modest.

## Slide 12: Program Administrator Cost of Saved Energy for Residential Programs Fairly Low for 2009-2011
Many of the more common program types cost two cents per kWh or less
Over 44% of residential electricity savings comes from lighting programs, which for 2009-2011 had a savings-weighted average cost to the program administrator of $0.007/kWh
Values in this figure are based on the 2009-2011 data in the LBNL DSM Program Impacts Database. CSE values are for program administrator costs and based on gross savings. Savings are levelized at a 6% real discount rate. The inter-quartile range and median CSE values are calculated for each program type.
Notes: Savings from residential programs are slightly more expensive, but the most prevalent program types – rebates on such consumer goods as lighting and appliances – remain fairly inexpensive with a savings-weighted average under one cent per kilowatt-hour. A large part of the explanation lies with lighting programs, which supplied more than 40% of residential sector savings and average $0.007/kWh.

## Slide 13: ESCO Industry Growth
• The ESCO industry continued to grow at a steady pace--despite the onset of a major recession--reporting revenues of approximately $5.3 billion in 2011.
• LBNL projects that the ESCO industry will grow from ~$4 billion (2008) to $7.5 billion (2014).
Notes: LBNL has been issuing reports on the energy services company (ESCO) industry since 1990; the chart and statistics on this slide are derived from LBNL’s 2013 “Current Size and Remaining Market Potential of the U.S. Energy Service Company Industry.”
LBNL defines an ESCO as a company for which performance contracting is a core business activity (i.e., service providers or installers who do not offer performance contracting are not included in this research). To estimate aggregate ESCO industry revenue, LBNL conducts interviews with ESCO executives, ESCO industry experts, and performs additional research. Reported revenues include energy efficiency performance contracting-related income as well as income from design/build activities, implementation contracting, etc. LBNL also asks ESCOs to project their revenues for future years, indicated above as light blue bars. LBNL believes this data collection effort covers a large majority of the overall ESCO industry, as defined above.
The chart above indicates steady growth of ESCO revenues over time, even during the most recent recession. It also shows that ESCO executives expect revenues to continue to grow, reaching $7.5 Bn by 2014.

## Slide 14: Estimates Suggest Large ESCO Market Potential Remains
• Remaining investment potential in facilities typically addressed by this industry ranges from ~$71 to $133 billion.
Notes: This analysis was introduced in LBNL’s 2013 “Current Size and Remaining Market Potential of the U.S. Energy Service Company Industry.” To understand the remaining investment potential in market segments traditionally served by ESCOs, LBNL estimated total square footage in each of these sectors and then surveyed ESCOs to understand how much square footage, of this total, had been addressed (served by their company) in the past 10 years. To estimate remaining investment potential, LBNL calculated 2012-normalized average and median costs per square foot for each segment using data from the over 4000 projects in its ESCO database. These average and median costs were multiplied by remaining square footage (i.e., square footage NOT served by an ESCO in the previous 10 years). The chart above shows the resulting total investment level remaining in each of seven segments historically served by ESCOs. The “high” and “low” scenarios result from application of both the average and median cost per square foot values. Across all segments, LBNL estimates that between $71 and $133 Bn of ESCO investment potential remains.

## Slide 15: CHP in the United States Today
DOE/ICF CHP Installation Database, 2013 Data
82.7 GW of installed CHP at over 4,300 industrial and commercial facilities (2013)
80% of capacity in industrial applications
70% of capacity is natural gas fired
Avoids more than 1.8 quadrillion Btus of fuel consumption annually
Avoids 241 million metric tons of CO2 compared to separate production
Notes:   DOE maintains a database of combined heat and power (CHP) installations in the US (available online at http://www.eea-inc.com/chpdata/). The database documents ownership information, year of first operation, location, sector/application, CHP technology type, capacity, and fuel type.
  DOE/ICF analysis above documents the total installed capacity (GW) of CHP installations across eight sectors/applications for 2013.

## Slide 16: National Progress Against 40 GW CHP Goal
Executive Order set a national goal of 40 GW of new CHP installation over the next decade
Newly installed: +1.6 GW
Internal ORNL/ICF Estimates for 2014-2016
Chart: Annual CHP Capacity Additions* (GW)
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015-2016
Existing CHP | 3.04 | 6.29 | 5.6 | 3.94 | 3.56 | 1.66 | 0.47 | 0.62 | 0.41 | 0.7 | 0.61 | 0.75 | 0.92 | 0.7
CHP Expected | 1.673 | 2.937
Notes: On August 30, 2012, President Obama signed Executive Order (E.O.) 13624 (http://www.gpo.gov/fdsys/pkg/FR-2012-09-05/pdf/2012-22030.pdf), establishing a national goal of 40 GW of new combined heat and power (CHP) capacity by 2020, a 50% increase over 2012 installed capacity.
In addition to setting a national goal, the E.O. directed the Departments of Energy, Commerce, and Agriculture as well as the Environmental Protection Agency to coordinate actions at the federal level to support combined heat and power in the industrial sector and to provide technical assistance to states to further this goal. Agencies are also directed to establish forums for best practice adoption and promotion of investment models that support CHP.
Since the E.O. was put in place, an additional 1.6 GW of CHP capacity have come online. ORNL/ICF project an additional ~4.5 GW by 2016.

## Slide 17: More Than Two-Thirds of States Have Adopted 2009 or Later Residential Codes
Notes: In recent years, partly driven by Recovery Act-funded initiatives, a number of states have adopted new or more stringent residential building energy codes. As of last month, about 65% of states have adopted codes at least as stringent as the 2009 IECC model code.

## Slide 18: 75% of States Have Adopted 2007 or Later Commercial Codes
Notes: Similarly, many states have adopted more stringent commercial building energy codes. While a number of states have no statewide commercial code, three-fourths of states have adopted codes at least as stringent as ASHRAE Standard 90.1-2007.

## Slide 19: Nearly 75% of States Are Engaged in Some Form of Compliance Enhancement
Source: BCAP
Notes: Nearly three-fourths of states also are engaged in some type of compliance enhancement, including DOE or non-profit studies of compliance and identification of gaps in code implementation; training for inspection and enforcement staff; or other compliance efforts driven by the states themselves or regional entities.

## Slide 20: Savings Rising Sharply as New End-Use Standards Take Effect
In 2012
Energy savings: 3.6 quads
CO2 emissions reduction: 198 million tons
Projected Total (cumulative through 2070)
Energy savings: 179 Quads
CO2 emissions reduction: ~10 billion tons
Consumer benefits (net present value): over $1 trillion
National Appliance and Equipment
Energy Efficiency Standards Adopted in 1987-2012
Chart: Annual Primary Energy Savings
| 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
NAECA 1987 | 0 | 0 | 0.0072514 | 0.013659 | 0.023722 | 0.04034 | 0.077404 | 0.12748 | 0.17998 | 0.23253 | 0.2909 | 0.34979 | 0.40202 | 0.45776 | 0.51635 | 0.56777 | 0.6062 | 0.64372 | 0.68 | 0.70814 | 0.72307 | 0.73641 | 0.73939 | 0.73624 | 0.72617 | 0.7304 | 0.71713 | 0.70118 | 0.68361 | 0.66475 | 0.6479 | 0.62848 | 0.61064 | 0.59498 | 0.58129 | 0.5561 | 0.52087 | 0.47895 | 0.43866 | 0.39986 | 0.36349 | 0.32745 | 0.29234 | 0.25872 | 0.22725 | 0.19924
EPAct 1992 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.035119 | 0.072516 | 0.13354 | 0.19788 | 0.26116 | 0.33294 | 0.3998 | 0.45914 | 0.49229 | 0.52451 | 0.55897 | 0.58821 | 0.61406 | 0.63925 | 0.65943 | 0.66446 | 0.67319 | 0.68222 | 0.69853 | 0.72013 | 0.6929 | 0.66447 | 0.59235 | 0.54373 | 0.49549 | 0.45619 | 0.41761 | 0.37916 | 0.34041 | 0.30035 | 0.25915 | 0.21668 | 0.17412 | 0.13111 | 0.087658 | 0.068375 | 0.05121
EPAct 2005 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.028962 | 0.068932 | 0.11316 | 0.15647 | 0.20644 | 0.24701 | 0.28692 | 0.32676 | 0.36405 | 0.40172 | 0.43779 | 0.47395 | 0.50963 | 0.54514 | 0.57863 | 0.58687 | 0.5937 | 0.60009 | 0.60613 | 0.61189 | 0.61743 | 0.62276 | 0.62804 | 0.63328 | 0.63849
EISA 2007 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.063646 | 0.14819 | 0.21679 | 0.28519 | 0.47806 | 0.67158 | 0.70176 | 0.7305 | 0.76031 | 0.79141 | 0.82284 | 0.85435 | 0.88633 | 1.2367 | 1.2657 | 1.2873 | 1.2913 | 1.2955 | 1.2986 | 1.3016 | 1.3043 | 1.3026 | 1.3013
DOE rulemakings | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0027015 | 0.021432 | 0.054048 | 0.086777 | 0.11819 | 0.14593 | 0.17462 | 0.20318 | 0.22842 | 0.26811 | 0.31535 | 0.36448 | 0.44341 | 0.52699 | 0.63365 | 0.74791 | 0.8576 | 0.96288 | 1.1202 | 1.2249 | 1.4729 | 1.6496 | 1.8615 | 2.0269 | 2.1637 | 2.2791 | 2.3839 | 2.4713 | 2.5605 | 2.6226 | 2.69 | 2.7418 | 2.7807 | 2.792 | 2.8075 | 2.83 | 2.8353 | 2.8497 | 2.8654
Notes: A series of legislative and administration initiatives since the mid 1980s have produced substantial savings from end-use standards for appliances, lighting and equipment. A recent LBNL report (Meyers, Stephen, Alison A. Williams and Peter Chan. Energy and Economic Impacts of U.S. Federal Energy and Water Conservation Standards Adopted from 1987 to 2012. LBNL 6217E. 2013) indicates that those savings have rising very sharply in recent years as the pace of rulemakings has quickened. Note that the savings impacts charted at left only include end-use standards adopted through 2012. More than 20 other standards are in various stages of development or rulemaking.

## Slide 21: Total Electricity Savings from Building Codes & End-Use Standards Risen Considerably
Chart: Total Electricity Savings as a Percent of Retail Sales (Withou C&S)
| Year | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012
Estimated End-Use Electricity Savings as % of Retail Sales Plus BEC and End-Use Savings | 0 | 0.0014131 | 0.0018832 | 0.0030258 | 0.0031451 | 0.0036652 | 0.003529 | 0.0034883 | 0.0035583 | 0.0032661 | 0.0036029 | 0.0027394 | 0.0027889 | 0.0029376 | 0.002691 | 0.0039442 | 0.0036137 | 0.0049536 | 0.0050607 | 0.0042308 | 0.0047668 | 0.01168
Total Estimated BEC End-Use Electricity Savings as % of Retail Sales Plus BEC and End-Use Savings | 0 | 0.0014554 | 0.0020343 | 0.0032427 | 0.0035141 | 0.0042851 | 0.0044472 | 0.0046253 | 0.0051095 | 0.0051102 | 0.0061356 | 0.0062781 | 0.0071344 | 0.0082041 | 0.008593 | 0.010778 | 0.011053 | 0.013304 | 0.014374 | 0.013627 | 0.014635 | 0.022331
Notes: The total estimated electricity-only savings from end-use standards and building energy codes, as a percent of total U.S. retail sales reported to the U.S. Energy Information Administration, are depicted above, drawing on estimates in the LBNL report and an October 2013 report by Pacific Northwest National Laboratory (Livingston et al., Building Energy Codes Program: National Benefits Assessment, 1992-2040. PNNL-22610). These savings estimates are stacked such that the top curve represents the combined estimated electricity savings from both codes and standards through 2012.

## Slide 22: Energy Use Disclosure Requirements
Location | Program Name or Ordinance | Effective Date | Market Segment | Trigger Event | Type of Requirement
States and Counties |  |  |  |  | 
Alaska | Residential Real Property Transfer Disclosure | 2008 | Single family, duplex and multifamily | Time of sale - prior to written offer as part of property disclosures | Disclosure - annual utility costs
Maine | Energy Efficiency Disclosure for Rental Units | 2006 | Rental units | Upon offering property for rent | Disclosure of building characteristics that affect energy useage
Montgomery County, Maryland | Utility Bill Disclosure | 2008 | Owner-occupied single family homes and condos | Time of sale - prior to contract signing | Disclosure of utility usage and costs
Nevada | SB 437, sections 31 and 50 | 2011 | Single family homes | Time of sale - prior to transaction close as part of property disclosures | Disclosure - comprehensive audit required, report includes improvement recommendations and estimated costs and payback
New York | Truth in Heating Law | 1981 | Single-family and multifamily - owner-occupied and rental | Time of sale or rental | Disclosure - heating and cooling bills
Notes: In 2011, LBNL researched energy use disclosure requirements. The table above is a 2011 snapshot that catalogues states and counties with energy use disclosure programs or ordinances. The following slide lists municipal ordinances or programs.

## Slide 23: Energy Use Disclosure Requirements (cont.)
Location | Program Name or Ordinance | Effective Date | Market Segment | Trigger Event | Type of Requirement
Cities |  |  |  |  | 
Berkeley, CA | Residential Energy Conservation Ordinance (RECO) | Updated 1992 | Single-family and multifamily - owner-occupied and rental | Time of sale or renovation ($50,000 or more) | Energy efficiency requirements
Chico, CA | Chapter 16.60 of the Chico Municipal Code | Updated 2010 | Single family and multifamily - owner-occupied and rental | Time of sale or transfer | Energy efficiency requirements
Chula Vista, CA | Increased Energy Efficiency Ordinance | 2010 | Single family and multifamily remodels | Time of remodel (building code) | Energy efficiency requirements above Title 24
Rohnert Park, CA | Ordinance No. 779 | 2007 | Low-rise single and multifamily additions | Time of remodel (building code) | Energy efficiency requirements above Title 24
San Francisco, CA | Residential Energy and Water Conservation Ordinance | Updated 1991 | Single family, multifamily and residential hotel renovations | Time of sale, renovation or condo conversion | Energy efficiency requirements
Boulder, CO | SmartRegs | 2011 | Rental properties: single family and multifamily | Prior to January 1, 2019 | Energy efficiency requirements
Chicago, IL | Disclosure of Heating Costs Ordinance Chapter 5-16 | 1987 | Rental units | Time of rental to new tenant | Disclosure of heating costs
Memphis, TN | Rental Ordinance 5292 | 2009 | Rental properties in which tenants pay utility bills | Upon request of tenant or discovery of excessive energy bills by Memphis Light, Gas and Water Division | Minimum energy efficiency standards and disclosure upon request
Austin, TX | The Energy Conservation Audit and Disclosure Ordinance (ECAD) | 2011 | All single family homes; multifamily buildings 10 years old or greater | Time of sale - before end of option period or at contract signing | Disclosure - energy audit required
Burlington, VT | Minimum Rental Housing Time of Sale Energy Efficiency Standards Ordinance | 1997 | Rental properties in which tenants pay utility bills | Time of sale of building | Energy efficiency requirements
Notes: The table above lists municipal disclosure ordinances or programs for municipalities as of 2011.

## Slide 24: On-Bill Programs: Large Volume and Generally Low Default Rates
Sector | Number of participants | Lifetime loan volume (nominal) | n= | Average size of loan | Median value and range of default rates | n=
Residential | 182,324 | $1.05B | 20 | $5,787 | 0.08% (0 to 3%) | 15
Non-residential | 50,339 | $775M | 7 | $15,400 | 0.9% (0.6 to 2.9%) | 7
Total | 232,663 | $1.83B | 27 | $7,867 |  | 22
As of January 2014, on-bill programs are operating or preparing to launch in the United States in at least 25 states, as well as in Canada and the United Kingdom.
In aggregate, the 30 programs reviewed by LBNL have delivered over $1.8 billion of financing to consumers for energy improvements over program lifetime.
Notes: Broadly, on-bill programs involve repaying financing for energy-related improvements on the consumer’s utility bill. Energy improvements may include a range of technologies that consumers can install on their premises: energy efficiency measures, distributed generation (e.g., solar photovoltaic, combined heat and power), and demand response (DR) technologies.
The 2014 SEE Action Report “Financing Energy Improvements on Utility Bills: Market Updates and Key Program Design Considerations for Policymakers and Administrators” surveyed 30 on-bill programs in the US, Canada, and the United Kingdom. The report, which was researched and written by LBNL staff, shows that over $1.8 Bn of capital has been deployed through on-bill mechanisms with generally low rates of default on the loans. The report describes the 30 programs against four program design considerations and offers key findings for each consideration:
- Disconnection and meter attachment;
- Sources of capital;
- Underwriting criteria; and
- Eligible measures.

## Slide 25: On-Bill Programs: New Statutory and Funding Support for Rural Efficiency Financing
Rural Energy Savings Plan (RESP)
Passed into law as part of the February 2014 Farm Bill, RESP will provide up to $75M annually from FY14-FY18 in zero percent interest loans to rural electric co-ops and municipal utilities to operate on-bill financing programs.
Energy Efficiency and Conservation Loan Program (EECLP)
Provides up to $250 million in FY 2014 for Treasury rate federal loans to support energy efficiency programs operated by co-ops and public power authorities serving rural areas. In FY2014, the EECLP has loan authority of up to $250 million, but in subsequent years, the program is uncapped, and will have access to a larger USDA loan authority of more than $6 billion per year. The EECLP supports on-bill financing programs, but also a wider range of projects including demand-side management and renewable energy investments.
Rural Energy for America Program (REAP)
Announced May 5, 2014, earmarks up to $12.3 million in grants and $57.8 million in loan guarantees. The REAP program targets farmers, ranchers and small business owners. It offers grants and loan guarantees covering up to 25 percent of project costs for a range of renewable energy and energy efficiency measures.
Notes: Three new USDA initiatives could fuel very substantial growth in the offering of on-bill financing among cooperatives. The Rural Energy Savings Plan (RESP), the Energy Efficiency Conservation Loan Program (EECLP), and the Rural Energy for America Program (REAP), can support on-bill financing. RESP and EECLP are modeled on South Carolina’s “Help My House” residential on-bill pilot (see Appendix of “Financing Energy Improvements on Utility Bills: Market Updates and Key Program Design Considerations for Policymakers and Administrators” for details of this program).
Once the implementation rules have been finalized, roughly 700 rural utilities for which USDA historically has financed power plants and transmission and distribution systems may apply for federal funds to either invest in the efficiency of their own infrastructure or pass along to their consumers in the form of loans for DSM projects that may be repaid through on-bill mechanisms.

## Slide 26: PACE Programs Spreading
Source: PaceNow.org
National PACE Landscape Today (PaceNow)
31 states and D.C. have enabled commercial PACE
25 active commercial PACE programs/platforms are ready to fund projects
7 active residential PACE programs
PACE is available in over 500 municipalities nationwide
Over $75 million is PACE financing extended to more than 250 commercial property owners
More than $250 million in applications from commercial property owners
Notes: PaceNow.org tracks states that have enacted or are considering property assessed clean energy (PACE)-enabling legislation as well as states where PACE programs are operational. PaceNow also active programs, number and value of projects funded, and project application pipelines by segment (residential versus commercial). See www.pacenow.org for more information.

## Slide 27: Revolving Loan Funds and Loan Loss Reserves Prevalent in Most States
Source: NASEO SELF database
NASEO SELF database
NASEO has tracked a total of 79 programs in 44 states, representing a total of over $2 billion in available state financing for energy efficiency and renewable energy projects in a variety of sectors.
LBNL’s forthcoming paper on ARRA-funded RLFs and LLRs, a collaboration with NASEO, will add to understanding of RLF and LLR programs.
Notes: NASEO’s State Energy Loan Fund (SELF) database tracks energy loan programs operated by State and Territory Energy Offices and their partners, and includes key statistics such as funding source, fund size, and program purpose. To date, NASEO has tracked a total of 79 programs in 44 states, representing a total of over $2 billion in available state financing for energy efficiency and renewable energy projects in a variety of sectors. NASEO’s recent report “Unlocking Demand: An Analysis of State Energy efficiency and Renewable Energy Financing Programs in the Buildings and Industrial Sectors” outlines major market barriers, success drivers, and models for state-led financing programs across the buildings and industrial sectors. See www.naseo.org for more information.
LBNL and NASEO are collaborating on a forthcoming report documenting quantitative results of ARRA-funded financing programs as well as qualitative themes and best practices learned by these programs.

## Slide 28: Green Banks and Secondary Market Deals Emerging as Important Tools
Source: Coalition for Green Capital
Green Banks
Secondary Market Transactions, Early Examples:
Craft3 (Oregon)
WHEEL (multiple states)
NYSERDA (New York)
Toledo (Ohio)
Keystone Help (PA)
CEFIA/Clean Fund (CT)
Western Riverside Council of Governments (CA)
Kilowatt Energy / Citi (emerging)
LBNL’s forthcoming paper on secondary markets for energy efficiency finance will explore these transactions in detail.
Notes: The Coalition for Green Capital (CGC) defines a green bank as a “public or quasi-public financing institution that provides low-cost, long-term financing support to clean, low-carbon projects by leveraging public funds through the use of various financial mechanisms to attract private investment so that each public dollar supports multiple dollars of private investment.” The Coalition for Green Capital tracks states’ interest in establishing a green bank; the figure above shows the states with which CGC has communicated and indicates their progress towards establishing a green bank. See http://www.coalitionforgreencapital.com/ for more information.
Several early examples of secondary market transactions of energy efficiency financing instruments exist, and will be explored in LBNL’s forthcoming paper “Accessing Secondary Markets as a Capital Source for Energy Efficiency Finance Programs: Program Design Considerations for Policymakers and Administrators.” Secondary markets and secondary market transactions have the potential to: replenish public or rate payer capital that seeded the financing program, reduce financing cost, reduce the need for program subsidies, demonstrate profitability for financial institutions, create a standardized asset class, and increase the overall amount of capital available to energy efficiency investment. The LBNL paper will explore this potential and make recommendations to program designers and administrators who are considering accessing the secondary market.
For a profile of the Craft 3 transaction, listed above, see LBNL’s “Selling an Energy Efficiency Loan Portfolio in Oregon: Resale of the Craft3 loan portfolio to Self-Help Credit Union” at http://emp.lbl.gov/sites/all/files/craft3-policy-brief_0.pdf.